## Slide 1: Estimating the global satellite-derived surface NH3 concentration
Zhenqi Luo 2020.11

## Slide 2: Estimation of surface NH3 concentration
Important in modelling the dry deposition of NH3
  Soil acidification
  Aquatic ecosystem eutrophication
  Drinking water contamination
  Form ammonium salt——particulate matters (PM)
    Air quality
    Human health
National monitoring programs: 2014
  NNDMN (2014~): China
  AMoN-China (2015~)
  AMoN-US: US
  EMEP: Europe
Satellite instruments
  IASI: 2008-2016
    daytime (09:30)
    processed into 0.25°×0.25° (arithmetic averaging method)
  AIRS
  CrIS
  TES
Chemistry transport models (CTMs)——GEOS-Chem (vertical profile and monthly averages): 2014
  Daily average and 9-10am average
  2°×2.5°×47level
  Meteorological filed data: GEOS-FP
  Emissions: EDGAR
    East Asia: MIX
    Europe: EMEP
    US: NEI
    Canada: CAC
    Biomass burning: FINNv1 (agricultural fires, wildfire and pre-scribed burning)
(Basto et al., 2015)
soil seed bank depletion by N pollution
(Kim et al., 2014)
Atmospheric N deposition to the South China Sea
Notes: Used the daytime IASI NH3 measurements due to the larger positive thermal contrast detected by satellite instruments leading to smaller errors compared to the nighttime data (Van Damme et al., 2014b).
The IASI NH3 columns used in this study were processed into the monthly data at 0.25° latitude × 0.25° longitude grids by the arithmetic averaging method (Van Damme et al., 2017;Whitburn et al., 2016;Liu et al., 2017a).

## Slide 3: Estimation of surface NH3 concentration
Step1: fit NH3 profile at each grid box——Gaussian function
    : NH3 concentrations at the layer height
    : the maximum NH3 concentrations at the height
    : an indicator for the spread or thickness of the NH3 concentrations
Step2: Extrapolate NH3 concentrations at any height——
Step3: Aggregated the IASI NH3 columns 𝛺𝐼𝐴𝑆𝐼(0.25°×0.25°) to the GEOS-Chem grid size (2°× 2.5°)——averaging method
    : the satellite-derived surface NH3 concentrations at a GEOS-Chem grid size at 9-10am
    : surface NH3 concentrations to NH3 columns calculated from GEOS-Chem
Step4: Downscale——satellite-derived scaling factor
    : the satellite-derived surface NH3 concentrations at a satellite IASI grid size (0.25°×0.25°) at 9-10am
    : scaling factor
Step5: Convert the instantaneous to daily average
    : daily average surface NH3 concentrations
    : the GEOS-Chem surface NH3 concentrations at the daily average to the average of 9-10 am.

## Slide 4: Results——satellite-derived surface NH3
NH3 vertical profiles from GEOS-Chem
  60°N and 55°S can be well modelled
Validation
  capture the general spatial pattern fairly well
  IASI-derived surface NH3 concentrations had better consistency than GEOS-Chem
    China
    the US
    Europe
Spatial distributions
  China——croplands (R2=0.65)
    eastern China
    Sichuan Basin
    northwestern Xinjiang
  US——croplands, livestock (SJV) (R2=0.30)
    Central US
    Eastern US
    Western coastal
  Europe——croplands (R2=0.17)
    Western
(Liu et al., 2019)

## Slide 5: Results——satellite-derived surface NH3
Seasonal variations
  China (ECH/SCH/GD)——Spring and summer (3-8)
    N fertilizer/manure application
    temperature in warm months
  Eastern US (EUS)——3-8, maximum in 5
    higher temperature
    emissions in vast croplands
  Western Europe——3-6
    higher temperature
    frequent N fertilization
the relationship with biomass burning
  CH1: crop straw burning
  CH2: the wetter climate and more frequent precipitation events
  US1: the forest fires or anthropogenic biomass burning
  US2: potential mineral N fertilization and anthropogenic biomass burning or forest fires
  EU1: the biomass burning and the agricultural fertilizations
  EU2: the biomass burning
Trends
(Liu et al., 2019)

## Slide 6: Questions?